Developing IP Multicast, Volume I

ISBN: 1-57870-077-9

Cisco Press

# Errata

Page 31, Figure 2-4

All addresses (in the box under "32 - IP Multicast Addresses")

that have a "128" in the second octet , should be changed to "129".

Thus, "224.128.1.1" would become "224.129.1.1", and so on.

Page 70, Figure 3-8

Figure 3-8 shows H3 sending a "Leave to 224.1.1.1" while it

should be shown sending IGMPv2 Membership report.

Page 95, Figure 4-7

Caption reads "VAT Site Information Window".

It should read "VIC Site Information Window".

Pages 94-98, Figures 4-5, 4-6, 4-7, 4-8 and 4-9

I received an Email from Jimmy Kyriannis whose NYU pictures were used

in the examples on VIC in this chapter.  He was very disappointed that

his proper name was not used (we substituted "Jill Smith") since we did

use his images.  I told him we would correct this in the next printing.

Please substitute all occurrences of "Jill Smith" in this section with

"Jimmy Kyriannis". Please note that Figure 4-7 has multiple occurrences

that need to be changed.

Page 113, Figure 5-5

The routing table of DVMRP router 2 (upper table) has the route to

network 15.10.0.0/16 via interface E0. The route should be via S0.

Page 134, Figure 6-2

Figure 6-2 shows R4 having interface S0 while Example 6-2 shows

that it does not have interface Serial0 but Serial1.  Change all

occurrences of "Serial1" to "Serial0" in Example 6-2.

Page 144, Last paragraph

Line 3 from the bottom reads that the Graft is sent to

"Router D" when it should read "Router C".

Page 168, First paragraph

The third line in the first paragraph reads "to pull the (S1, G)

traffic". It should read "to pull the (S2, G) traffic"

Page 181, The first line of the note

the first occurences of CBT and PIM-SM should be exchanged to read

"Note that PIM-SM differs from CBT in that ..."

Page 183, 9th line from the bottom

The JOIN-TIMEOUT should be 17.5, not 7.5 seconds

Page 233, Example 10-5

Example 10-5 does not show interface Serial0 in the list of

outgoing interfaces for the group (*, 224.2.127.254) which

it should according to the Dense Mode Rule 1.  Change the (*,G)

entry in Example 10-5 to:

(*, 224.2.127.254), 00:04:10/00:00:00, RP 0.0.0.0, flags: D

Incoming interface: Null, RPF nbr 0.0.0.0

Outgoing interface list:

Serial0, Forward/Dense, 00:04:10/00:00:00

Ethernet0, Forward/Dense, 00:04:10/00:00:00

Page 246, Last line in the section "PIM-SM Outgoing Interface Timers"

The last line in this paragraph reads "according to the first

item in PIM-SM Rule 5.". Instead of "first" it should read

"second".

Page 252, Table 11-3, second row

The second row in table 11-3 discusses about the meaning of

"Forward/Sparse". Delete the sentence "Because this entry is in

the outgoing interface list of a dense mode (*, G) entry, it always

reflects forward and dense mode."

Page 253, Table 11-4

The second row in table 11-4 has 00:00:40/00:02:53 as an

example time, while the second row on the same page has

00:00:40/00:02:20. The both values should be 00:00:40/00:02:20

Page 255, Table 11-7, flag "F Register flag"

Delete the note in parenthesis at the bottom of this table entry

that begins, "(Note: The F flag is set on the parent (*,G) entry...)".

Page 274, Second paragraph, third line

The third line in the second paragraph reads "Step 9". It should

read "Step 7".

Page 294, First paragraph, fourth line

The fourth line in the first paragraph starts with "solid arrows)".

It should read "dashed arrows)".

Page 316, First paragraph, last line

The last line in the first paragraph reads "where inadvertently

not updated.". The "where" should be "were".

Page 332, Last paragraph, first line

The first line in the last paragraph reads "group range of

239.255.0.0-239.255.255.255". The range should be

"239.254.0.0-239.254.255.255".