Advanced IP Network Design

ISBN: 1-57870-097-3

Cisco Press

# Errata

Page 70 – The Router B configuration at the bottom of the page should read:

Interface e0

ip address 172.16.9.2 255.255.255.0

standby ip 172.16.9.1

standby priority 20

standby preempt

Page 71 – The Router D configuration at the top of the page should read:

Interface e0

ip address 172.16.9.3 255.255.255.0

standby ip 172.16.9.1

standby priority 10

standby preempt

The first sentence of the last paragraph should read, “When Router B’s serial interface fails, it

will decrease its standby priority to 30, and Router D will take over as the HSRP active router.”