Cisco OSPF Command and Configuration Handbook

ISBN: 1-58705-071-4

Cisco Press

# Errata

Page 84 – Regarding the Router B routing table:

rtrB#show ip route,  the second line in the second half of the configuration should read:

O    1.1.1.1 [110/65] via 10.1.1.1, 00:01:01, Serial0

Page 193 – Regarding Figure 6-3, the configuration that reads:

Loopback 0

51.51.51.51/24, should be changed to Loopback 1

Page 289 – The second sentence under the ‘Purpose’ heading should read, “The router with the highest

non-zero priority will be elected the DR.”

Page 310 – The fourth sentence under the ‘Purpose’ heading should read, “This command will redistribute

only classful routes into OSPF if the subnets keyword is not used.”

Regarding Figure 14-1, please add the ‘bandwidth 64’ statement under the serial interfaces.

Page 321 - The fourth sentence under the ‘Purpose’ heading should read, “This command will redistribute

only classful routes into OSPF if the subnets keyword is not used.”

Page 322 – Regarding Figure 14-3, please add the ‘bandwidth 64’ statement under the serial interfaces.

Page 325 – Regarding the middle of the page, the metric output for 10.1.1.4 should be 20, not 200.

Page 415 – Regarding the Router B configuration contained in the top table, please add the following to the

configuration:

frame-relay-map ip 10.1.1.3 110 broadcast

Regarding the Router C configuration contained in the top table, please add the following to the

configuration:

frame-relay-map ip 10.1.1.2 120 broadcast