***Scenario 1-1 Configurations

Scenario 1-1 Switch-A Configuration

hostname Switch-A

Scenario 1-1 Switch-B Configuration

set system name Switch-B

***Scenario 1-2 Configurations

Scenario 1-2 Switch-A Configuration

hostname Switch-A

service timestamps log datetime localtime show-timezone

!

enable secret cisco

!

logging on

logging 192.168.1.100

logging trap notifications

logging facility local0

no logging console

logging monitor critical

logging buffered 256000 debug

!

ip domain-name lanps.com

ip name-server 192.168.1.100 192.168.1.200

ip domain-lookup

!

interface vlan 1

no shutdown

ip address 192.168.1.10 255.255.255.0

!

ip default-gateway 192.168.1.1

!

snmp-server community readme ro

snmp-server community writeme rw

snmp-server contact Bob Jones (508)1112222

snmp-server location 999 1st Street, Boston, MA

snmp-server host 192.168.1.100 readme

snmp-server enable traps

!

line con 0

password cisco

line vty 0 15

password cisco

Scenario 1-2 Switch-B Configuration

set system name Switch-B

!

set interface sc0 192.168.1.20 255.255.255.0

!

set ip route default 192.168.1.1

!

set ip dns enable

set ip dns domain lanps.com

set ip dns server 192.168.1.100 primary

set ip dns server 192.168.1.200

!

set snmp community read-only readme

set snmp community read-write writeme

set snmp community read-write-all

set snmp trap 192.168.1.100 readme

set snmp trap enable

!

set logging level all notifications default

set logging server 192.168.1.100

set logging server severity notifications

set logging server facility local0

set logging history 10

set logging history severity debug

set logging server enable

set logging console disable

set logging buffer 100

***Scenario 1-3 Configurations

Scenario 1-3 Switch-A Configuration

hostname Switch-A

service timestamps log datetime localtime show-timezone

!

enable secret cisco

!

logging on

logging 192.168.1.100

logging trap notifications

logging facility local0

no logging console

logging monitor critical

logging buffered 256000 debug

!

ip domain-name lanps.com

ip name-server 192.168.1.100 192.168.1.200

ip domain-lookup

!

define interface-range WORKSTATION-PORTS fastEthernet0/2 – 24

!

no mls qos

!

system mtu 1546

!

interface fastEthernet0/1

description ROUTER-A

speed 10

duplex half

!

interface range fastEthernet0/2 – 24

description WORKSTATION-PORTS

speed auto

duplex auto

!

interface gigabitEthernet0/1

no speed nonegotiate

flowcontrol receive desired

flowcontrol send desired

!

interface vlan 1

no shutdown

ip address 192.168.1.10 255.255.255.0

!

ip default-gateway 192.168.1.1

!

snmp-server community readme ro

snmp-server community writeme rw

snmp-server contact Bob Jones (508)1112222

snmp-server location 999 1st Street, Boston, MA

snmp-server host 192.168.1.100 readme

snmp-server enable traps

!

line con 0

password cisco

line vty 0 15

password cisco

Scenario 1-3 Switch-B Configuration

set system name Switch-B

!

set interface sc0 192.168.1.20 255.255.255.0

!

set ip route default 192.168.1.1

!

set ip dns enable

set ip dns domain lanps.com

set ip dns server 192.168.1.100 primary

set ip dns server 192.168.1.200

!

set snmp community read-only readme

set snmp community read-write writeme

set snmp community read-write-all

set snmp trap 192.168.1.100 readme

set snmp trap enable

!

set logging level all notifications default

set logging server 192.168.1.100

set logging server severity notifications

set logging server facility local0

set logging history 10

set logging history severity debug

set logging server enable

set logging console disable

set logging buffer 100

!

set port negotiation 1/1 enable

set port flowcontrol send 1/1 desired

set port flowcontrol receive 1/1 desired

!

set port name 2/1 SERVER-A

set port speed 2/1 100

set port duplex 2/1 full

Scenario 1-3 Router-A Configuration

hostname Router-A

!

enable secret cisco

!

interface Ethernet0/0

no shutdown

ip address 192.168.1.1 255.255.255.0

!

line vty 0 4

password cisco

***Scenario 1-4 Configurations

Scenario 1-4 Switch-A Configuration

hostname Switch-A

service timestamps log datetime localtime show-timezone

!

clock timezone NZST 12

clock summer-time NZDT recurring first Sunday October 02:003 Sunday March 02:00 60

!

ntp server 192.168.1.1

ntp authentication-key 1 md5 cisco123

ntp trusted-key 1

ntp authenticate

!

enable secret cisco

!

logging on

logging 192.168.1.100

logging trap notifications

logging facility local0

no logging console

logging monitor critical

logging buffered 256000 debug

!

ip domain-name lanps.com

ip name-server 192.168.1.100 192.168.1.200

ip domain-lookup

!

define interface-range WORKSTATION-PORTS fastEthernet0/2 – 24

!

no mls qos

!

system mtu 1546

!

interface fastEthernet0/1

description ROUTER-A

speed 10

duplex half

!

interface range fastEthernet0/2 – 24

description WORKSTATION-PORTS

speed auto

duplex auto

!

interface gigabitEthernet0/1

no speed nonegotiate

flowcontrol receive desired

flowcontrol send desired

!

interface vlan 1

no shutdown

ip address 192.168.1.10 255.255.255.0

!

ip default-gateway 192.168.1.1

!

snmp-server community readme ro

snmp-server community writeme rw

snmp-server contact Bob Jones (508)1112222

snmp-server location 999 1st Street, Boston, MA

snmp-server host 192.168.1.100 readme

snmp-server enable traps

!

line con 0

password cisco

line vty 0 15

password cisco

Scenario 1-4 Switch-B Configuration

set system name Switch-B

!

set timezone NZST 12

set summertime recurring first Sunday October 02:00 third Sunday March 02:00 60

set summertime enable NZDT

!

set ntp client enable

set ntp server 192.168.1.1 key 1

set ntp key 1 trusted md5 cisco123

set ntp authentication enable

!

set interface sc0 192.168.1.20 255.255.255.0

!

set ip route default 192.168.1.1

!

set ip dns enable

set ip dns domain lanps.com

set ip dns server 192.168.1.100 primary

set ip dns server 192.168.1.200

!

set snmp community read-only readme

set snmp community read-write writeme

set snmp community read-write-all

set snmp trap 192.168.1.100 readme

set snmp trap enable

!

set logging level all notifications default

set logging server 192.168.1.100

set logging server severity notifications

set logging server facility local0

set logging history 10

set logging history severity debug

set logging server enable

set logging console disable

set logging buffer 100

!

set port negotiation 1/1 enable

set port flowcontrol send 1/1 desired

set port flowcontrol receive 1/1 desired

!

set port name 2/1 SERVER-A

set port speed 2/1 100

set port duplex 2/1 full

Scenario 1-4 Router-A Configuration

hostname Router-A

!

clock timezone NZST 12

!

ntp master

ntp authentication-key 1 md5 cisco123

ntp trusted-key 1

ntp authenticate

!

enable secret cisco

!

interface Ethernet0/0

no shutdown

ip address 192.168.1.1 255.255.255.0

!

line vty 0 4

password cisco