***No Configurations for Scenario 10-1 thru Scenario 10-4

***Scenario 10-5 Configuration Part 1 (SPAN)

Scenario 10-5 Switch-A Configuration Part 1 (SPAN)

hostname Switch-A

!

enable secret cisco

!

vtp mode transparent

!

vlan 2

name VLAN2

!

monitor session 1 source interface fastEthernet0/2 both

monitor session 1 destination interface fastEthernet0/3

!

interface fastEthernet0/1

switchport trunk encapsulation dot1q

switchport mode trunk

switchport nonegotiate

!

interface fastEthernet0/2

switchport mode access

switchport access vlan 2

!

interface fastEthernet0/3

switchport mode access

!

interface vlan 1

no shutdown

ip address 192.168.1.1 255.255.255.0

!

line vty 0 4

password cisco

Scenario 10-5 Switch-B Configuration Part 1 (SPAN)

set system name Switch-B

!

set vtp mode transparent

!

set vlan 2 name VLAN2

set vlan 2 2/2

!

set trunk 2/1 nonegotiate dot1q

set trunk 2/2 off

set trunk 2/3 off

!

set span 2/1 2/3 both filter 2 inpkts enable create

!

set interface sc0 192.168.1.2 255.255.255.0

***Scenario 10-5 Configuration Part 2 (VSPAN)

Scenario 10-5 Switch-A Configuration Part 2 (VSPAN)

hostname Switch-A

!

enable secret cisco

!

vtp mode transparent

!

vlan 2

name VLAN2

!

monitor session 1 source vlan fastEthernet0/2 rx

monitor session 1 destination interface fastEthernet0/3 ingress vlan 1

!

interface fastEthernet0/1

switchport trunk encapsulation dot1q

switchport mode trunk

switchport nonegotiate

!

interface fastEthernet0/2

switchport mode access

switchport access vlan 2

!

interface fastEthernet0/3

switchport mode access

!

interface vlan 1

no shutdown

ip address 192.168.1.1 255.255.255.0

!

line vty 0 4

password cisco

***Scenario 10-5 Configuration Part 3 (RSPAN)

Scenario 10-5 Switch-A Configuration Part 3 (RSPAN)

hostname Switch-A

!

enable secret cisco

!

vtp mode transparent

!

vlan 2

name VLAN2

!

vlan 100

remote-span

!

monitor session 1 source interface fastEthernet0/2 rx

monitor session 1 destination remote vlan 100 reflector-port fastEthernet0/24

!

interface fastEthernet0/1

switchport trunk encapsulation dot1q

switchport mode trunk

switchport nonegotiate

!

interface fastEthernet0/2

switchport mode access

switchport access vlan 2

!

interface fastEthernet0/3

switchport mode access

!

interface vlan 1

no shutdown

ip address 192.168.1.1 255.255.255.0

!

line vty 0 4

password cisco

Scenario 10-5 Switch-B Configuration Part 3 (RSPAN)

set system name Switch-B

!

set vtp mode transparent

!

set vlan 2 name VLAN2

set vlan 2 2/2

set vlan 100 name VLAN100 rspan

!

set trunk 2/1 nonegotiate dot1q

set trunk 2/2 off

set trunk 2/3 off

!

set rspan destination 2/3 100 inpkts enable create

!

set interface sc0 192.168.1.2 255.255.255.0

***Scenario 10-5 Configuration Part 4 (RSPAN)

Scenario 10-5 Switch-A Configuration Part 4 (RSPAN)

hostname Switch-A

!

enable secret cisco

!

vtp mode transparent

!

vlan 2

name VLAN2

!

vlan 100

remote-span

!

monitor session 1 source remote vlan 100

monitor session 1 destination interface fastEthernet0/3 ingress vlan 1

!

interface fastEthernet0/1

switchport trunk encapsulation dot1q

switchport mode trunk

switchport nonegotiate

!

interface fastEthernet0/2

switchport mode access

switchport access vlan 2

!

interface fastEthernet0/3

switchport mode access

!

interface vlan 1

no shutdown

ip address 192.168.1.1 255.255.255.0

!

line vty 0 4

password cisco

Scenario 10-5 Switch-B Configuration Part 4 (RSPAN)

set system name Switch-B

!

set vtp mode transparent

!

set vlan 2 name VLAN2

set vlan 2 2/2

set vlan 100 name VLAN100 rspan

!

set trunk 2/1 nonegotiate dot1q

set trunk 2/2 off

set trunk 2/3 off

!

set rspan source 2/2 100 rx

!

set interface sc0 192.168.1.2 255.255.255.0

***Scenario 10-5 Configuration Part 5 (VACL)

Scenario 10-5 Switch-A Configuration Part 5 (VACL)

hostname Switch-A

!

enable secret cisco

!

vtp mode transparent

!

vlan 2

name VLAN2

!

vlan 100

remote-span

!

interface fastEthernet0/1

switchport trunk encapsulation dot1q

switchport mode trunk

switchport nonegotiate

!

interface fastEthernet0/2

switchport mode access

switchport access vlan 2

!

interface fastEthernet0/3

switchport mode access

!

interface vlan 1

no ip address

!

interface vlan 2

ip address 192.168.2.1 255.255.255.0

!

line vty 0 4

password cisco

Scenario 10-5 Switch-B Configuration Part 5 (VACL)

set system name Switch-B

!

set vtp mode transparent

!

set vlan 2 name VLAN2

set vlan 2 2/2

set vlan 100 name VLAN100 rspan

!

set trunk 2/1 nonegotiate dot1q

set trunk 2/2 off

set trunk 2/3 off

!

set security acl ip TELNET permit tcp any any eq telnet capture

set security acl ip TELNET permit any

set security acl capture-ports 2/3

set security acl map TELNET 2

!

commit security acl all

!

set interface sc0 192.168.1.2 255.255.255.0