***Scenario 6-1 Configurations

Scenario 6-1 Switch-A Configuration

set system name Switch-A

!

set vtp mode transparent

set vtp domain lanps

!

set vlan 2 name VLAN2

set vlan 2 2/3

!

set mls enable

set mls include 192.168.1.1

set mls flow destination-source

set mls agingtime 480

set mls agingtime fast 128 7

!

set interface sc0 192.168.1.10 255.255.255.0

!

set trunk 2/1 nonegotiate isl

Scenario 6-1 Router-A Configuration

hostname Router-A

!

enable secret cisco

!

mls rp ip

!

interface fastEthernet0/0

no shutdown

!

interface fastEthernet0/0.1

encapsulation isl 1

ip address 192.168.1.1 255.255.255.0

ip access-group 100 in

mls rp vtp-domain lanps

mls management-interface

mls rp ip

!

interface fastEthernet0/0.2

encapsulation isl 2

ip address 192.168.2.1 255.255.255.0

mls rp vtp-domain lanps

mls rp ip

!

access-list 100 permit tcp any any eq telnet

access-list 100 deny ip any any log

!

line vty 0 4

password cisco

***Scenario 6-2 Configurations

Scenario 6-2 Switch-A Configuration

set system name Switch-A

Scenario 6-2 Switch-A-MSFC Configuration

hostname Switch-A-MSFC

!

enable secret cisco

!

interface vlan 1

no shutdown

ip address 192.168.1.1 255.255.255.0

!

interface vlan 2

ip address 192.168.2.1 255.255.255.0

!

router ospf 1

network 192.168.1.0 0.0.0.255 area 0

network 192.168.2.0 0.0.0.255 area 0

!

line vty 0 4

password cisco

Scenario 6-2 Router-A Configuration

hostname Router-A

!

enable secret cisco

!

interface ethernet 0

no shutdown

ip address 192.168.1.2 255.255.255.0

!

interface loopback 0

ip address 10.0.0.1 255.0.0.0

!

router ospf 1

network 10.0.0.0 0.255.255.255 area 0

network 192.168.1.0 0.0.0.255 area 0

!

line vty 0 4

password cisco

***Scenario 6-3 Configurations

No configurations for this scenario

***Scenario 6-4 Configurations

Scenario 6-4 Switch-A Configuration

hostname Switch-A

!

enable secret cisco

!

vtp mode transparent

!

vlan 2

name VLAN02

!

interface fastEthernet 2/1

no shutdown

switchport

!

interface fastEthernet 2/2

no shutdown

switchport

switchport access vlan 2

!

interface fastEthernet 2/3

no shutdown

switchport

!

interface vlan 1

no shutdown

ip address 192.168.1.1 255.255.255.0

!

interface vlan 2

ip address 192.168.2.1 255.255.255.0

!

router ospf 1

network 192.168.1.0 0.0.0.255 area 0

network 192.168.2.0 0.0.0.255 area 0

!

line vty 0 15

password cisco

Scenario 6-4 Router-A Configuration

hostname Router-A

!

enable secret cisco

!

interface ethernet 0

no shutdown

ip address 192.168.1.2 255.255.255.0

!

interface loopback 0

ip address 10.0.0.1 255.0.0.0

!

router ospf 1

network 10.0.0.0 0.255.255.255 area 0

network 192.168.1.0 0.0.0.255 area 0

!

line vty 0 4

password cisco