CompTIA Network+ N10-007 Cert Guide

First Edition

Copyright © 2018 Pearson Education, Inc.

ISBN-10: 0789759810
ISBN-13: 9780789759818

Warning and Disclaimer

Every effort has been made to make this book as complete and as accurate as possible, but no warranty or fitness is implied. The information provided is on an "as is" basis. The author and the publisher shall have neither liability nor responsibility to any person or entity with respect to any loss or damages arising from the information contained in this book or from the use of the CD or programs accompanying it.

When reviewing corrections, always check the print number of your book. Corrections are made to printed books with each subsequent printing.

First Printing: February 2018

Corrections for December 22, 2021

| Pg. | Error – First Printing | Correction |
| --- | --- | --- |
| 496 | Network Layer Troubleshooting: Solution, Step 2 reads: The decimal value of the third octet in the subnet mask is 224. Therefore, the block size is 32 (that is, 256 – 224 = 32). | Should read: The decimal value of the fourth octet in the subnet mask is 224.Therefore, the block size 32 (that is, 256 – 224 = 32). |
| 496 | Network Layer Troubleshooting: Solution, Step 3 reads: The first subnet is 192.168.1.0/27 (192.168.1.0/27 with the three borrowed bits in the third octet set to 0). | Should read: The first subnet is 192.168.1.0/27 (192.168.1.0/27 with the three borrowed bits in the fourth octet set to 0)." |

Corrections for November 25, 2019

| Pg. | Error – First printing | Correction |
| --- | --- | --- |
| 125 | Table 4-2 (rows 8, 9), reads: 1000BASE-LX MMF 5 km 1000BASE-SX SMF 5 km | Should read: 1000Base-SX MMF 550 m. 1000Base-LX SMF 5 km. |

Corrections for October 12, 2018

| Pg. | Error – First printing | Correction |
| --- | --- | --- |
| Chapter 6, pg. 222 | In the section on SNAT it reads: This is often called a “many-to-one” mapping. | Should read: This is often called a “one-to-one” mapping. |

This errata sheet is intended to provide updated technical information. Spelling and grammar misprints are updated during the reprint process, but are not listed on this errata sheet.