# CCNA Portable Command Guide, Second Edition

First Edition

Copyright © 2008 Cisco Systems, Inc.

ISBN-10: 1-58720-193-3
ISBN-13: 978-1-58720-193-6

Warning and Disclaimer

Every effort has been made to make this book as complete and as accurate as possible, but no warranty or fitness is implied. The information provided is on an "as is" basis. The author and the publisher shall have neither liability nor responsibility to any person or entity with respect to any loss or damages arising from the information contained in this book or from the use of the CD or programs accompanying it.

When reviewing corrections, always check the print number of your book. Corrections are made to printed books with each subsequent printing.

First Printing: July 2007

Corrections for all Printings

## Page 28, VLSM Section

You need only four of them. You can hold the rest for future expansion or recombine them for a new, larger subnet:

00010000 = .16/30

00010100 = .20/30

00011000 = .24/30

00011100 = .32/30

.

.

.

00111000 = .56/30

00111100 = .60/30

The first four of these can be combined into the following:

00010000 = .16/28

The rest of the /30 subnets can be combined into two /28 networks:

00100000 = .32/28

00110000 = .48/28

Or these two subnets can be combined into one larger /27 network

00100000 = .32/27

Going back to the original table you now have the following:

| 00000000 = | .0/26 | Cannot use because it has been subnetted |
| --- | --- | --- |
| 00000000 = | .0/30 | Network E |
| 00000100 = | .4/30 | Network F |
| 00001000 = | .8/30 | Network G |
| 00001100 = | .12/30 | Network H |
| 00010000 = | .16/28 | Future Growth |
| 00100000 = | .32/27 | Future Growth |
| 01000000 = | .64/26 | Network A |
| Table is correct | From this | Point forward |

Figure Corrections

Page 37 –	Figure 4-4 should read 4-1

Page 38 –	Figure 4-5 should read 4-2

Page 64 –	Figure 6-5 should read 6-1

Page 78 –	Figure 8-7 should read 8-1

Page 87 –	Figure 9-8 should read 9-1

Page 98 –	Figure 10-9 should read 10-1

Page 121 –	Figure 12-2 should read 12-1

Page 132 –	Figure 13-3 should read 13-1

Page 148 –	Figure 14-4 should read 14-1

Page 153 –	Figure 14-5 should read 14-2

Page 162 –	Figure 15-6 should read 15-1
Figure 15-7 should read 15-2

Page 163 –	Figure 15-8 should read 15-3
Figure 15-9 should read 15-4

Page 164 –	Figure 15-10 should read 15-5
Figure 15-11 should read 15-6

Page 165 –	Figure 15-12 should read 15-7

Page 166 –	Figure 15-13 should read 15-8
Figure 151-14 should read 15-9

Page 167 –	Figure 15-15 should read 15-10
Figure 15-16 should read 15-11

Page 168 –	Figure 15-17 should read 15-12

Page 169 – Figure 15-18 should read 15-13
Figure 15-19 should read 15-14

Page 170 – Figure 15-20 should read 15-15

Page 171 –	Figure 15-21 should read 15-16
Figure 15-22 should read 15-17

Page 172 – Figure 15-23 should read 15-18

Page 173 –	Figure 15-24 should read 15-19
Figure 15-25 should read 15-20

Page 174 –	Figure 15-26 should read 15-21
Figure 15-27 should read 15-22

Page 175 –	Figure 15-28 should read 15-23
Figure 15-29 should read 15-24

Page 176 –	Figure 15-30 should read 15-25
Figure 15-31 should read 15-26

Page 177 –	Figure 15-32 should read 15-27
Figure 15-33 should read 15-28

Page 178 –	Figure 15-34 should read 15-29
Figure 15-35 should read 15-30

Page 179 –	Figure 15-36 should read 15-31
Figure 15-37 should read 15-32

Page 180 –	Figure 15-38 should read 15-33
Figure 15-39 should read 15-34

Page 181 –	Figure 15-40 should read 15-35
Figure 15-41 should read 15-36

Page 228 –	Figure 23-3 should read 23-1

Page 233 –	Figure 24-4 should read 24-1

Page 254 – Figure 26-1, first Network listing:

should read Network 172.16.10.0/24

Page 261 –	Figure 27-2 should read 27-1

Page 280 –	Figure 28-3 should read 28.1

Page 17 – The Enhanced Bob Maneuver

Last line reads:

126	62	30	14	6	4	N/A	Number of Valid Subnets

Last line should read:

126	62	30	14	6	2	N/A	Number of Valid Subnets

Page 32 – Figure 3-2 chart headings

Reads:

/21	/22	/23	/21

Should read:

/21	/22	/23	/24

Page 33 – Figure 3-3 char headings

Reads:

/21	/22	/23	/21

Should read:

/21	/22	/23	/24

Page 118 – First NOTE

Reads:

This method is the only way to configure extended-range VLANs (VLAN IDs from 100 to 4094).

Should read:

This method is the only way to configure extended-range VLANs (VLAN IDs from 1006 to 4094).

This errata sheet is intended to provide updated technical information. Spelling and grammar misprints are updated during the reprint process, but are not listed on this errata sheet.