CCNA Security Portable Command Guide

First Edition

Copyright © 2012 Cisco Systems, Inc.

ISBN-10: 1-58720-448-7
ISBN-13: 978-1-58720-448-7

Warning and Disclaimer

Every effort has been made to make this book as complete and as accurate as possible, but no warranty or fitness is implied. The information provided is on an "as is" basis. The author and the publisher shall have neither liability nor responsibility to any person or entity with respect to any loss or damages arising from the information contained in this book or from the use of the CD or programs accompanying it.

When reviewing corrections, always check the print number of your book. Corrections are made to printed books with each subsequent printing.

First Printing: May 2012

Corrections – January 22, 2015

| Pg | Error – Second Printing | Correction |
| --- | --- | --- |
| 135 | Chapter 11, First set of Command under Figure 11-1, Fourth Command down Reads: R1(config)#access-list 100 permit ip any host 209.165.200.254 eq 80 | Should read: R1(config)#access-list 100 permit tcp any host 209.165.200.254 eq 80 |

Corrections – August 2, 2012

| Pg | Error | Correction |
| --- | --- | --- |
| 242 | Chapter 17, Mirror VPN Notepad Reads: Empty | Should read: The mirror configuration should only be used as a guide when configuring the peer. The following configuration MUST NOT be directly applied to the peer device. crypto isakmp policy 2 authentication pre-share encr aes 128 hash sha group 5 lifetime 86400 exit crypto isakmp policy 1 authentication pre-share encr 3des hash sha group 2 lifetime 86400 exit crypto isakmp key cisco123 address 209.165.200.225 crypto ipsec transform-set R1-->R3-Transform-Set esp-sha-hmac esp-aes 128 mode tunnel exit ip access-list extended SDM_1 remark CCP_ACL Category=4 remark IPSec Rule permit ip 192.168.3.0 0.0.0.255 192.168.1.0 0.0.0.255 exit crypto map SDM_CMAP_1 1 ipsec-isakmp description Apply the crypto map on the peer router's interface having IP address 209.165.202.129 that connects to this router. set transform-set R1-->R3-Transform-Set set peer 209.165.200.225 match address SDM_1 exit |

This errata sheet is intended to provide updated technical information. Spelling and grammar misprints are updated during the reprint process, but are not listed on this errata sheet.