***Scenario 2-2 Configurations

Scenario 2-2 Switch-A Configuration

set system name Switch-A

set vtp mode off

Scenario 2-2 Switch-B Configuration

hostname Switch-B

vtp mode transparent

***Scenario 2-3 Configurations

Scenario 2-3 Switch-A Configuration

set system name Switch-A

!

set vtp mode off

!

set vlan 10 name Engineering

set vlan 20 name Sales

set vlan 30 name Marketing

!

set vlan 10 2/1-16

set vlan 20 2/17-32

set vlan 30 2/33-48

!

set trunk 2/1-48 off

Scenario 2-3 Switch-B Configuration

hostname Switch-B

!

vtp mode transparent

!

vlan 10

name Engineering

vlan 20

name Sales

vlan 30

name Marketing

!

interface range fastEthernet0/1 – 16

switchport mode access

switchport access vlan 10

!

interface range fastEthernet0/17 – 32

switchport mode access

switchport access vlan 20

!

interface range fastEthernet0/33 – 48

switchport mode access

switchport access vlan 30

***Scenario 2-4 Configurations

Scenario 2-4 Switch-A Configuration

set system name Switch-A

!

set vtp mode off

!

set vlan 10 name Engineering

set vlan 20 name Sales

set vlan 30 name Marketing

!

set vlan 10 2/1-16

set vlan 20 2/17-32

set vlan 30 2/33-48

!

set interface sc0 10 192.168.10.1 255.255.255.0

Scenario 2-4 Switch-B Configuration

hostname Switch-B

!

vtp mode transparent

!

vlan 10

name Engineering

vlan 20

name Sales

vlan 30

name Marketing

!

interface range fastEthernet0/1 – 16

switchport mode access

switchport access vlan 10

!

interface range fastEthernet0/17 – 32

switchport mode access

switchport access vlan 20

!

interface range fastEthernet0/33 – 48

switchport mode access

switchport access vlan 30

!

interface vlan 10

ip address 192.168.10.1 255.255.255.0

***Scenario 2-5 Configurations

Scenario 2-5 Switch-A Configuration

set system name Switch-A

!

set vtp mode off

!

set vlan 10 name Engineering

set vlan 20 name Sales

set vlan 30 name Marketing

!

set vlan 10 2/1-16

set vlan 20 2/17-32

set vlan 30 2/33-48

set vlan 4000 2/3

!

set spantree macreduction enable

!

set interface sc0 10 192.168.10.1 255.255.255.0

Scenario 2-5 Switch-B Configuration

hostname Switch-B

!

vtp mode transparent

!

vlan 10

name Engineering

vlan 20

name Sales

vlan 30

name Marketing

vlan 4000

!

spanning-tree extend system-id

!

interface range fastEthernet0/1 – 2, fastEthernet0/4 - 16

switchport mode access

switchport access vlan 10

!

interface fastEthernet0/3

switchport mode access

switchport access vlan 4000

!

interface range fastEthernet0/17 – 32

switchport mode access

switchport access vlan 20

!

interface range fastEthernet0/33 – 48

switchport mode access

switchport access vlan 30

!

interface vlan 10

ip address 192.168.10.1 255.255.255.0