# CCNA Flash Cards and Exam Practice Pack Errata

Inside Front Cover:

To study for the CCNA 640-801 exam, it says to read: Chapters 1, 2, 4, 6, 9, and 10 in Part 1; all of Part 2.

Readers should also read Chapter 11 in Part I for their preparation.

Page 26, Question 22 Answer

The answer should be:

The data link layer translates packets from the network layer into frames for transport onto the physical medium, and it lets the network layer control the interconnection of data circuits within the physical layer.

Page 48, Question 11 Answer

The answer should be:

A bus and ring topology connects all devices by a single cable. This cable connects from one computer to another. In a logical bus and a single ring topology, only one packet can be sent at a time.

Pages 80 and 81

Change all references of ‘shielded twisted pair’ to shielded twisted-pair

Page 140, Question 17 Answer

Replace (192.168.0.3:1023)  with  (192.168.0.2:1025)

Page 193, Question 20

The question should read:

What modem standard provides up to 56 kbps of downstream data transfer and up to 33.6 kbps of upstream data transfer?

The answer should be:

V.90 is the modem standard that provides up to 56 kbps of downstream data transmission and up to 33.6 kbps of upstream data transmission.

Page 324, Question 46 Answer

The answer should be:

The forward delay is the time it takes a port to move from a listening state to a learning state and then from a learning state to a forwarding state. The default time is 15 seconds for each state. A bridge will spend a total of 30 seconds to transition from listening to forwarding states.