CCNP Quick Reference

First Edition

Copyright © 2008 Cisco Systems, Inc.

ISBN-10: 1-58720-236-0
ISBN-13: 978-1-58720-236-0

Warning and Disclaimer

Every effort has been made to make this book as complete and as accurate as possible, but no warranty or fitness is implied. The information provided is on an "as is" basis. The author and the publisher shall have neither liability nor responsibility to any person or entity with respect to any loss or damages arising from the information contained in this book or from the use of the CD or programs accompanying it.

When reviewing corrections, always check the print number of your book. Corrections are made to printed books with each subsequent printing.

First Printing: June 2008

Corrections for all Printings

| Pg | Error | Correction |
| --- | --- | --- |
| 28 | Chapter 3, OSPF Metric, Last sentence Reads: The cost is a 16-bit number, so it can be any value from 1 to 65,535. Router(config-router)#ip ospf cost 27 | Should read: The cost is a 16-bit number, so it can be any value from 1 to 65,535. Router(config-if)#ip ospf cost 27 |
| 45 | Chapter 4, Second Sentence on page Reads: The DIS is elected based on priority, with MAC address as the tie breaker (the lowest number wins for both priority and MAC address). | Should read: The DIS is elected based on priority, with MAC address as the tie breaker (the highest number wins for both priority and MAC address). |

| 181 | Chapter 2, ADSL, First Paragraph, Third Sentence Reads: A splitter takes the incoming analog signals and splits off the frequencies under 4MHz to a voice line. | Should read: A splitter takes the incoming analog signals and splits off the frequencies under 4KHz to a voice line. |
| --- | --- | --- |

This errata sheet is intended to provide updated technical information. Spelling and grammar misprints are updated during the reprint process, but are not listed on this errata sheet.